## Slide 1: Fundamentals of Engineering Thermodynamics Chapter 3 Evaluating Properties
Nick DiFilippo
5/21/2015

## Slide 2: Phase and Pure Substances
3 phases (liquid, solid, vapor)
Pure substances
Phase changes
  Vaporization
  Melting
  Sublimation
Two phases
  Liquid-Vapor
  Solid-Liquid
  Solid-Vapor

## Slide 3: State Principle
For a simple compressible system, two independent intensive thermodynamics properties will fix the values of all other intensive thermodynamics properties

## Slide 4: 3.2 P-V-T Surface
Axes
1 phase Regions
2 phase regions
3 phase region
Saturation lines
Critical Point

## Slide 5: Projections of PVT surface

## Slide 6
T-v Diagram
Quality x :

## Slide 8: Thermodynamic Property Tables
Steam Tables (A-2) – (A-6)
Table A-2 and Table A-3 Saturation Table ( be careful with units!)

## Slide 9: Thermodynamic Property Tables
Table A-4 Superheated Table
Table A-5 Compressed Liquid Table

## Slide 10: Thermodynamic Property Tables
Tables (A-7) – (A-9) Refrigerant 22
Tables (A-10) – (A-12) Refrigerant 134a
Tables (A-13) – (A-15) Ammonia
Tables (A-16) – (A-18) Propane
Need to use approximation if these are compressed liquids.

## Slide 12: Evaluation of Properties in S-L Mixture Region
Specific volume :
Internal energy :
Enthalpy :
v of water with quality of 0.9 at 100 C
p of water at 100 C and specific volumes of a) 2.434m3/kg b) 1.0m3/kg and c) 1.0423 x10-3 m3/kg
Linear Interpolation Example: Specific volume of water at 10 bar and 215 C

## Slide 13: Double Interpolation Example
Find specific enthalpy (h) of a superheated steam at a temperature of 325 C and a pressure of 5.70 bar

## Slide 14: Example: Complete the Table
Temp. ( oC) | Pressure (kPa) | u (kJ/kg) | x | Phase | 
120 |  |  |  | Sat. vapor | 
50 | 80 |  |  |  | 
30 |  |  | 0.5 |  | 
 | 300 | 2713.1 |  |  | 
Temp. ( oC) | Pressure (kPa) | u (kJ/kg) | x | Phase | 
120 | 198.5 | 2529.3 | 1 | Sat. vapor | 
50 | 80 | 209.32 | ---- | Comp. Liquid | 
30 | 4.246 | 1271.19 | 0.5 | mixture | 
240 | 300 | 2713.1 | ------- | Super. Vapor | 
Liquid = H2O (water)

## Slide 15: Specific Heats
Specific Heats of Common Substances can be found in Table A-19
In an incompressible substance

## Slide 16: The Ideal Gas Equation of State
R is the gas constant and is different for each gas
Universal Gas Constant R = 8.314 kJ/kmol*k
(Table 3.1)

## Slide 17
Employ the Ideal Gas Equations

## Slide 18: Is Water Vapor an Ideal Gas?

## Slide 19: Compressibility Factor
Correction Factor
Ideal gas Z = 1
Normalize Pressure and Temperature
Reduced Pressure:
Reduced Temperature
Was ideal gas a good approximation in example?

## Slide 20: Generalized Compressibility Chart
Appendix Fig A-1 , A-2, A-3
PR: 0-1 , 0,10 , 10-40

## Slide 21: Example:
Given: Find the specific Volume of R-134a at 140oC and 1.6MPa
Find: Specific volume using three methods (Ideal Gas Law, Compressibility Chart, and Z chart)
0.02103 m3/kg (10.3% error)
0.0187 m3/kg (1% error)
Z = 0.89 v = 0.0.187 m3/kg

## Slide 22
A tank contains 0.05 m3 of Nitrogren at (-21oC) and 10 Mpa. Determine the mass of nitrogen in kg using a)the ideal gas model
B) compressibility chart

## Slide 23: Internal Energy Enthalpy and Specific Heat of Ideal Gases

## Slide 24: Polytropic Process of Air as an Ideal Gas
Air undergoes a polytropic compression in a piston cylinder assembly from p1 = 1 bar , T1 = 22 C to p2 = 5 bars. Employing the ideal gas model, determine the work and hear transfer per unit mass if n = 1.3

## Slide 25: Example

## Slide 26: Example 2

## Slide 27: Example 3
A tank fitted with an electrical resistor holds 2 kg of nitrogen initially at 27 C, 0.1 MPa. Over a period of 10 minutes, electricity is provided to the resistor at a rate of 0.12 kW. During the same time, a heat transfer of magnitude 12.59 kJ occurs from nitrogen to the ambient. Assume the idea gas behavior, determine the final temperature, in C and pressure, in MPa of the gas.