## Slide 1: MCE 341- Engineering Thermodynamics
Nick DiFilippo
Summer Session 1
5/19/2015

## Slide 2: What is Thermodynamics?

## Slide 3: Energy
Conservation of Energy
1st Law of Thermodynamics
2nd Law of thermodynamics

## Slide 4: History
Thomas Savery
1698
Thomas Newcomen
1712
Lord Kelvin
William Thompson
Rudolf Clausius
William Rankine
Emergence of the 1st and 2nd laws
Mid 1800’s

## Slide 5: Defining Systems
System- What we want to study
Surroundings- mass or region outside of the system being studied
Boundary – Separates system from surrounding

## Slide 6: Closed vs. Open Systems
Closed System:
Energy can be transferred.
Mass cannot be transferred
Isolated System:
Energy cannot be transferred
Mass cannot be transferred
Open System (Control Volume) :
Energy can be transferred
Mass can be transferred

## Slide 7: Control Volumes

## Slide 8: Properties
Any Characteristic of a system
Intensive Properties – Independent of Mass
  (temperature, density, pressure)
Extensive Properties – Depends on size
  (total mass, total volume)

## Slide 9: State, Process, and Equilibrium
State - Condition of a system by its properties
Process - A system undergoes a process when its properties change
Equilibrium – balance
Steady State

## Slide 10: Review of Units
SI Units
English Units
What is the force of 1 lbm

## Slide 11: Density and Specific Volume
Density (ρ) – mass per unit volume
Specific Volume (ν) volume per unit mass

## Slide 12: Temperature
Zeroth Law of Thermodynamics
Thermal Equilibrium
Celsius, Fahrenheit, Kelvin , Rankine
T(C) = T(K) - 273.15
T(F) = T(R) – 459.67
T(F) = 9/5 T(C) - 32

## Slide 13: Pressure
Normal force exerted by a fluid per unit area
SI Units
Bar , Pascal (Pa), MPa, kPa
1 bar = 105 Pa
1 atm = 101.325 kPa = 1.01325 bar
English
psi
1 atm = 14.696psi
Gage Pressure, Absolute Pressure, and Vacuum Pressure

## Slide 14: Chapter 2 – First Law of Thermodynamics
First Law of Thermodynamics
Energy Balance of Closed Systems

## Slide 15: Kinetic Energy
P
Units (kJ) or (Btu) 1kJ = 103 N*m
1Btu = 778 ft*lbf
Potential Energy
Internal Energy

## Slide 16: Energy transfer by Heat
Q – modes of heat transfer (Conduction, Convection, Radiation)
Q > 0 : heat is transferred into the system
Q < 0 : heat is transferred out of the system
W > 0 : work is done by the system
W < 0 : work is done on the system
Work
Q = SQin – SQout ,
W = SWout – SWin

## Slide 17
Energy Balance can be applied to a single process from 1 to 2:
Or applied to multiple processes from 1 to 2 to 3:
Or applied to closed cycle from 1 to 2 to 3 to 1:
Expansion or compression work:

## Slide 18
2.6 Cycle Energy Balance
Power Cycle
Refrigeration Cycle

## Slide 19
Polytropic Process Relation
n = 0 constant pressure process; n = constant volume process;
n = 1 constant temperature process

## Slide 20
Example 2.1

## Slide 21
Example 2.2